## Slide 1: Mini-I/O Field Installable Cable Connector
Ruud van den Brink
GPM Industrial Communications
2021-03-08
INSTRUCTION: Cover image below may be replaced in the slide master with another image from either the Images Library PowerPoint provided along with this template OR a licensed image which meets TE’s photography guidelines to meet user’s requirement. Delete this instruction in final presentation.

## Slide 2: Agenda
Introduction to Mini-I/O
Standardization & Standards
Typical Mini-I/O Applications
Field Installable Cable Connector
How to Apply the Mini-I/O FI Cable Connector

## Slide 3: Introduction to Mini-I/O
Summary
Mini-I/O is a ruggedized, miniaturized connector family suited for Serial, Bus, Ethernet communication
Wide area of applications, incl. Cabinets, Distributed peripherals, Robotics, Machinery, Drive and Motor Applications
Technology
IEEE 802.3 standards from 10 Mbps to 10 Gbps
Connector standard series IEC 61076-3-122
Benefits
Cost-effective, toolless, error free installation
Compact connector design (25% of the size of RJ45)
Integrated power (PoE)
Dual contact point contact technology guarantees good shock and vibration properties
Next steps:
Drive adoption into the industrial market through standardization and user groups
Succesively introduce other Mini-I/O FI cable connecotrs for different wire and cable diameters
Product launches in FY20/FY21

## Slide 4: Mini-I/O Product Family
R/A and vertical Board Connectors
Type 1 and Type II
Solder and piercing cable connectors
Type 1 and Type II
Mini-I/O Cord sets
Type 1 and Type II
https://www.te.com/commerce/DocumentDelivery/DDEController?Action=srchrtrv&DocNm=1-1773703-8_MINI_IO&DocType=DS&DocLang=EN
https://www.te.com/commerce/DocumentDelivery/DDEController?Action=showdoc&DocId=Data+Sheet%7F7-1773983-5%7F2006%7Fpdf%7FEnglish%7FENG_DS_7-1773983-5_2006.pdf
Link to product flyer:
Link to virtual sample kit:

## Slide 5: Industrial Mini-I/O Connector Advantages

## Slide 6: Connector Interface Type I and Type II
Industrial Mini I/O has 2 unique interfaces which may be used by customers to prevent mis-mating
Key customer benefit is that using this interface physically prevents improper network hook up with other standard RJ45 networks
Customers may also use this interface for physical identification of critical networks (i.e. safety)
Other coding variants are possible
D-SHAPE TYPE 1
U-SHAPE TYPE 2
Can not mis-mate
Type I:
D-shape
Type II:
U-shape

## Slide 7: Secure Interface Locking System
Accidental unplugging of a network connection due to shock, vibration, pulling on cords, etc.. Causes expensive down time in an industrial environment
Industrial Mini I/O’s unique locking system has a pull out force greater than 100N
Header lock leaf
Plug lock projection
Lock ejector

## Slide 8: PCB Header Designed for Board Strength
The other part to secure a lasting connection is proper board retention
This header design has 2 features to enable required retention strength
  Solder pads at 5 points
  3 pegs with through hole anchor
  Plastics are LCP based, improving co-planarity, supporting reflow soldering and giving it a MSL1
①
②
① Solder pad at 5 points
② Peg has through hole anchor (3/5)
Solder pads are used to fix the SMT connector to a PCB. Generally this is done at 2 points. Industrial Mini-I/O has 5 points enhancing the retention force and preventing connector tilt.

## Slide 9: Mini-I/O Contact System Designed for Reliability
Known as the “Fighting Snake Principle”
Multiple points of contact reduce contact failures
Au plated products improve conductivity and contact lifespan
Overall design = Improved Reliability for Customer Networks
Cable Side Contact
PCB Side Contact
Contact Cross Section
2 points of contact

## Slide 10: Other Mini-IO Advantages
Industrial Mini-I/O is a reliable compact wire to board connector system for Industrial Communications. It is 25% of the original size of an RJ45.
Blue: Industrial Mini-I/O Connector
Green: RJ45 Connector

## Slide 11: Industrial Mini-I/O Family
R/A and vertical Board Connectors
Type 1 and Type II
Solder and piercing cable connectors
Type 1 and Type II
Mini-I/O Cord sets
Type 1 and Type II
  Hand tool is available for wire termination and cable crimp
Wire termination
Cable crimp
Cat6A Field Installable Cable
Connectors
Type 1 and Type II

## Slide 12: Standardization & Standards

## Slide 13: Mini-I/O Standard
The IEC61076-3-122 Mini-I/O standard defines two classes.
Shock
Vibration
Voltage Proof
Class B: New performance requirements for frequencies up to 500 MHz in addition to the performance requirements up to 100 MHz provided with the previous edition ED1

## Slide 14: Typical Mini-I/O Applications

## Slide 15: CPS Applications & Connectivity Requirements
 | Cabinet | Distributed Peripherals | Robot & Machine | Drive & Motor
Miniaturized connectors | Small slice widths / high packaging densities | Compact devices | Limited space inside robots and machines | Compact devices
IP code | IP20 | IP20 except near humid processes | IP20 | IP20 except near humid processes
High temperatures | Machine cabinets | Devices attached to robots or machines | Heat-generating processes (e.g. welding) | Rotation
Resilience vs. shock & vibration |  |  | Repetitive movements and sudden changes of direction | Periodical rotation and sudden changes of direction
Resilience vs. EM noise | Alien crosstalk from neighboring cables | Rotating machinery and wireless communication | Rotating machinery | 
Field- installability | Variable cable lengths |  | N/A (pre-assembled ready-to-install cables) | Variable cable lengths

## Slide 16: Mini-IO Application Areas & Use Cases
 | General Discrete Manufacturing | Automative Manufacturing | Process Industry | Energy Generation Facilities | Rail
Backbone |  |  |  |  | 
M2M |  |  |  |  | 
Cabinet |  |  |  |  | 
Field |  |  |  |  | 
IoT |  |  |  |  | 
Application Areas
Use Cases
Mini-IO application areas
Distributed Peripherals
Source: Siemens
Cabinet
Robot & Machine
Drive & Motor
Source: Yaskawa

## Slide 17: Field Installable Cable Connector

## Slide 18: Features, Advantages, Benefits

## Slide 19: Mini-I/O FI Part Numbers

## Slide 20: How to Apply the Mini-I/O FI Cable Connector

## Slide 21: Application of the Mini-I/O Field Installable Connector

## Slide 23: Other Mini-I/O FI variants (as part of the modular concept)
135 degrees Cable Outlet
90 degrees Cable Outlet

## Slide 24: Demo Kit Industrial Mini-I/O: TE PN 2368065-1